## Slide 1
A Theoretically Guaranteed Deep Optimization Framework for Robust Compressive Sensing MRI
AAAI-19: Thirty-Third AAAI Conference on Artificial Intelligence
Risheng Liu 1,2,* Yuxi Zhang 1,2 Shichao Cheng 2,3 Xin Fan 1,2 Zhongxuan Luo 1,2,3,4
1. DUT-RU International School of Information Science & Engineering, Dalian University of Technology, Dalian, China
2. Key Laboratory for Ubiquitous Network and Service Software of Liaoning Province, Dalian, China
3. School of Mathematical Science, Dalian University of Technology, Dalian, China
4. Institute of Artificial Intelligence, Guilin University of Electronic Technology, Dalian, China
Dalian University of Technology Feb. 1th, 2019

## Slide 2
Motivation

## Slide 3
Motivation MRI
Slow acquisition
Artifacts introducing
Expensive calculation
Magnetic Resonance Imaging (MRI)
None-invasive
Anatomical information

## Slide 4
Motivation CS-MRI
Signal processing based MRI reconstruction
Much lower sampling rate than Nyquist rate
Preserving image quality
Compressive Sensing MRI (CS-MRI)
under-sampling operation
fast Fourier transform
sparse K-space data
desired MR image
data
acquisition
Optimization
Loss/Fidelity
Prior/Regularization
reconstruction

## Slide 5
Model Optimization
Motivation Image processing in multimedia
Hyper-Laplacian prior
Non-local similarity prior
Total variation prior
Dark channel prior
Hand-crafted
priors
Highly ill-posed
Require additional skills
High computational cost

## Slide 6
Model Optimization
Motivation Image processing in multimedia
Learnable
priors
No theoretical guarantee
Data dependent
Rely on architecture
MRF prior
Denoise CNN prior
Discriminative prior

## Slide 7
Motivation Image processing in multimedia
Stage 1
Stage 2
......
Stage T
Optimization
Physical principles and priors
Theoretical derivation
White box
High computational cost
Less flexibility and capability
Model Optimization

## Slide 8
Motivation Image processing in multimedia
Neural networks
Fast forward process
Data driven
Severe data dependence
Weak interpretability
Instable inference
End-to-end
LeNet-5
AlexNet
ResNet
FractalNet
VGG16
VGG19

## Slide 9
Motivation Image processing in multimedia
Hybrid framework
Model based principles
Data driven information
No guarantee on convergence
Sacrificing model based information
Model Optimization
Stage 1
Stage 2
......
Stage T
?

## Slide 10
Reconstruction Process
Sparse K-space Data
Reconstructed MRI
Reconstruction of CS-MRI
Motivation CS-MRI
sparse representation (TV et.al)
wavelet transform (PBDW et.al)
dictionary learning (FDLCP et.al)
non-local method (PANO et.al)
deep learning based (DAGAN et.al)

## Slide 11
Motivation problems in existing methods
Model based methods
Model based prior
Satisfying restoration accuracy
High computational cost
Deep learning based methods
Fast feed-forward process
Data driven prior
Lower flexibility and robustness
Hybrid process based methods
Efficiency improvement
No guarantee on convergence
Sacrificing model based information
Convergence
Efficiency
Robustness
Accuracy

## Slide 12
Our Paradigm for CS-MRI
A Theoretically Guaranteed Deep Optimization Framework
for Robust Compressive Sensing MRI

## Slide 13
Our Paradigm contributions
Fidelity Module——Reconstruction
Data-driven Module——Artifacts removal
Optimal Condition Module——Error control
Prior Module——Details restoration
sparse code of x: wavelet basis () trade-off parameter
CS-MRI optimization model
Framework composition
Sparsity regularization

## Slide 14
Our Paradigm Fidelity Module
Closed form solution
current restoration
Rough reconstruction
A balance between the current restoration and the fidelity term
A correction by the fidelity when the output is out of the desired descent direction
Artifacts introducing
Effects

## Slide 15
Our Paradigm Data-driven Module
Residual learning network
Realizing Artifacts removal
Utilizing Data dependent information utilizing
Providing Fast forward pass process
No guarantee on convergence
Effects

## Slide 16
Our Paradigm Optimal Condition Module
Feedback mechanism based on momentum proximal gradient
Have the similar convergence conclusion with the traditional first-order optimality methods, even with deep architecture
Effects
Theorem
The sequence generated by our algorithm converges to a critical point of the original objective function.

## Slide 17
Our Paradigm Prior Module
Residual learning network
Enhancing the effect of sparse prior regularization
Correcting over-smooth problem
Revealing more details
Effects

## Slide 18
Our Paradigm Pipeline
Input
Zero-filled image
Fidelity module
Rough reconstruction
Data-driven module
Artifacts removal
Prior module
Details restoration
Convergence guarantee

## Slide 19
Our Paradigm Experiments

## Slide 20
Our Paradigm Experiments
Highest reconstruction accuracy
Lowest reconstruction error
Strongest robustness to variation of sampling patterns and ratios
Ability to handle different sampling ratios and sampling patterns

## Slide 21
Our Paradigm Experiments
Comparison of Execute Time (s)
Sampling Rate | Data | ZF | TV | SIDWT | PBDW | PANO | FDLCP | ADMM-Net | BM3D-MRI | Ours
10% | T1w | 0.0035 | 2.0098 | 14.8269 | 45.2639 | 27.9626 | 84.8494 | 1.2332 | 10.8777 | 0.3167
 | T2w | 0.003 | 2.3625 | 20.9462 | 53.0273 | 42.9235 | 84.1869 | 1.2349 | 9.5716 | 0.3631
50% | T1w | 0.0032 | 0.7631 | 5.5761 | 26.1274 | 11.1466 | 83.068 | 1.2499 | 11.5394 | 0.5633
 | T2w | 0.0036 | 0.7013 | 5.7678 | 24.8526 | 14.4659 | 81.8903 | 1.2445 | 10.6671 | 0.5545
Notice that ADMM-Net and ours are tested on GPU.
The proposed framework can ideally provide a efficient reconstruction process and comes to the fastest method among the competitors.

## Slide 22
Our Paradigm Experiments
Visualization comparison

## Slide 23
Our Paradigm Experiments
Robust to various kinds of testing data
Data | ZF | TV | SIDWT | PBDW | PANO | FDLCP | ADMM-Net | BM3D-MRI | Ours
Chest | 22.95 | 24.43 | 24.17 | 25.91 | 27.73 | 26.84 | 25.38 | 26.27 | 28.22
Cardiac | 23.40 | 29.17 | 27.49 | 31.34 | 33.14 | 33.84 | 31.42 | 31.44 | 35.69
Renal | 24.32 | 28.77 | 27.66 | 31.05 | 32.21 | 33.74 | 31.13 | 31.01 | 34.79

## Slide 24
Our Paradigm Experiments
Robust to Rician noise pollution
  our method has a better noise tolerance than the others,

## Slide 25
CS-MRI with Rician Noise Rician Noise
MRI scanners acquire complex data where both real and imaginary parts are corrupted with zero-mean uncorrelated Gaussian noise with equal variance.
The calculation of the magnitude image transforms the original complex Gaussian noise into Rician noise.
Rician Noise for magnitude MR image
Rician Noise
Guassian Noise
noisy image - clean image
Rician Noise
noisy image - clean image
Rician noise is not additive noise

## Slide 26
CS-MRI with Rician Noise Optimization
Noisy image reconstruction
Clear image reconstruction
Alternating over two sub-problems
Learnable architecture for Rician noise removal
Rician noise
Gaussian noise
Clean image
ResNet 1
ResNet 2

## Slide 27
CS-MRI with Rician Noise Experiments
Comparison with classical Rician noiser remover
The choice of taking our learnable architecture as denoiser performs better than that of taking RiceOptVST.

## Slide 28
CS-MRI with Rician Noise TwoNets_CS+Denoising
Comparison with traditional CS-MRI methods followed by a denoiser
Data | Denoiser | Zero-Filling | TV | SIDWT | PBDW | PANO | FDLCP | ADMM-Net | BM3D-MRI | Ours
T1w | RiceOptVST | 24.11 | 25.51 | 25.78 | 26.65 | 27.08 | 20.71 | 26.36 | 27.36 | 28.05
 | Ours | 24.62 | 25.71 | 25.94 | 26.83 | 27.30 | 25.42 | 26.49 | 27.64 | 
T2w | RiceOptVST | 25.40 | 27.83 | 28.37 | 29.13 | 29.22 | 20.34 | 29.14 | 29.67 | 30.77
 | Ours | 26.36 | 28.20 | 28.68 | 29.46 | 29.64 | 27.21 | 29.45 | 30.34 | 
Notes: 该图比较了“先重建后去噪”（A+B）与我们提出的迭代框架（A○B）的性能。
横坐标为B选RiceOptVST的情况，纵坐标为B选TwoNets的情况，黄色三角形”Ours“表示A○B的情况，
可以看出对于A+B的形式，B选取TwoNets时重建结果更好，而A○B形式的重建结果则比A+B好

## Slide 29
Conclusions
Efficiency
Deep optimization algorithms for CS-MRI reconstruction
Accuracy
Both model based and data dependent prior knowledge are utilized
Convergence
Automatic checking and feedback mechanism for error-control
Robustness
Extended scheme for real-world CS-MRI with Rician noise.

## Slide 30
Thanks
rsliu@dlut.edu.cn
yuxizhang@mail.dlut.edu.cn
shichao.cheng@outlook.com
xin.fan@dlut.edu.cn
zxluog@dlut.edu.cn
AAAI-19: Thirty-Third AAAI Conference on Artificial Intelligence